AltaNet ETH41 4G WiFi

SELLING KEY

Selling Point: ETH41 is a powerful indoor CPE, with built-in Mini-PCIe interface inside. Support LTE modules both TDD and FDD, or multi-mode wireless access with various of modules Support LTE both TDD and FDD or multi-mode modules Standard mini-PCIe interface Support VPN IP Sec, PPTP Sec, L2TP Sec. Support 3.3V standard USIM card Support 802.11 b/g/n with antenna 2x2 inside Up to 25 users access to WiFi Support IPv4/IPv6 Support MAC Filter, IP Filter, URL Filter

Specifications ITEM DESC CPE Parameters Platform ROM+RAM 16MB+32MB Chipset Qualcomm AR9341 Interface Mini-PCIe Comply to mini-PCIe interface standard CEM1.2,can be accessed in a variety of LTE module or Wimax-LTE dual-mode module Ethernet Port one 10/100Mbps WAN port, one 10/100Mbps LAN port, two RJ45 port Voice POTS One FXS RJ11 port USIM Slot Support 3.3V USIM Power Input: universal range 110-240V AC; Output: 12V/1A DC Button Power Switch Mini rocker switch Reset/Reboot YES VPN IP Sec, PPTP Sec, L2TP Sec. WIFI Support 802.11b/g/n with 2x2 MIMO antenna inside ,300Mbps, 2.4GHz Wireless Security WEP, WPA2,WPA-Personal LTE Antenna 1T2R, support high gain antenna built-in or outside DMZ Support LED Indicator Power, Mode, Internet, WiFi Working Temperature -10℃~45℃ Dimensions 184x166x42 mm Module Parameters Description Support TDD-LTE, FDD-LTE,UMTS,GSM, support voice, data and internet by internal LTE/UMTS/GSM module with Mini PCIE interface Platform ROM+RAM: 16+32MB Chipset: Qualcomm MDM9x15/MDM9x25 Specification Refer to LM111A/LM111C/LM112MD/LM113MD/LM121A/LM122M AT Instruction Support standard AT instruction set